## Slide 1
Design of a More Powerful Wind Turbine Blade
Edward Biegert, Andres Goza, Miguel Ibarra, Ara Parsekian
Advisors: Dr. David McStravick, Dr. Brent Houchens
Final Design
Iterative Solver:
We have built an iterative solver in Visual Basic and MATLAB which uses a Blade Element Momentum (BEM) program, WT_Perf, to optimize parameters:
Blend – how the airfoil (cross-sectional shape) varies along the blade length
Taper – how the chord length (width) of the blade varies along the length
Twist – how the airfoils rotate along the blade length
Results
Power Considerations
  Optimized twist, taper, and blend
  Potential to outperform current blades in market
  Structural Considerations
  Optimization process accounts for bending moment
  Allows for long fatigue life
Introduction
Wind energy is on the rise
  $21 billion invested in 2009*
  39% of new U.S. power in 2009*
  Government subsidies through 2012*
  In order to take advantage of trends in the wind energy industry, we have designed a 90 m diameter wind turbine blade to produce more power at lower wind speeds than existing designs while addressing structural considerations.
  We constructed an iterative solver in order to optimize certain parameters in the blade design.
Acknowledgements:
We gratefully acknowledge the help and guidance of our advisors, without whom this work would never have been possible
We also thank Vestas for their financial and technical support
*2009 Wind Technologies Market Report
For a given blend distribution, adjust taper
For a given taper, adjust twist
Establish blend distributions
Linear
Quadratic
Square
Exponential
Select root and tip airfoils
Calculate coefficient of power and bending moment using WT_Perf, assign a score
Compare scores and adjust parameters to maximize score
Obtain optimized blade
Iterative Solver
Optimum Blade
Linear Taper
Root Airfoil: NACA 2418
High Lift, Structural Rigidity
Tip Airfoil: NACA 63-418
Medium Lift, Low Drag
Blend Distribution
0 = Root Airfoil, 1 = Tip Airfoil
Chart: r/R
| 0.14500000000000005 | 0.23500000000000001 | 0.32500000000000012 | 0.41500000000000009 | 0.505 | 0.59500000000000008 | 0.68500000000000016 | 0.77500000000000013 | 0.86500000000000021 | 0.95500000000000018
Blend | 0 | 0.002 | 0.012 | 0.048 | 0.11 | 0.196 | 0.308 | 0.444 | 0.604 | 0.79
Twist Distribution
Chart: r/R
| 0.14500000000000005 | 0.23500000000000001 | 0.32500000000000012 | 0.41500000000000009 | 0.505 | 0.59499999999999997 | 0.68500000000000005 | 0.77500000000000024 | 0.86500000000000021 | 0.95500000000000018
Twist | 24 | 14 | 6 | 5 | 0 | -1.6 | -1.6 | -1.6 | -5 | -0.5442
Turbine Performance
Tested using WT_Perf at 15 rpm
Chart: Wind Speed (m/s)
| 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Wind Speed (m/s) | 17.706 | 214.801 | 486.84 | 844.503 | 1289.24 | 1815.963 | 2351.982 | 2875.201