## Slide 1
1
2
3
1 Mass driver provides constant driving force
4 Aluminum housing protects gear system
5 Acrylic housing protects device and supports syringe
2 Pendulum oscillates with constant frequency and controls flow rate
3 Gears translate pendulum oscillation into downward motion on syringe
1
2
3
4
5
NeoSyP: Neonatal Syringe Pump for the Developing World
Elizabeth Carstens1, Yiwen Cui1, Rashmi Kamath1, Clare Ouyang1, Cynthia Sung2
1Bioengineering, 2Mechanical Engineering and Materials Science
teamzikomo@gmail.com
References and Acknowledgements:
Machen, H. Personal Interview at Oshman Engineering Design Kitchen. 04 Oct. 2010.
This project is funded through Beyond Traditional Borders which is made possible by a grant to Rice University from the Howard Hughes Medical Institute through the Undergraduate Science Education Program. The design work for this project is supported by the resources of the Oshman Engineering Design Kitchen. We would especially like to thank Dr. Maria Oden, Dr. Renata Ramos and Dr. Elizabeth Molyneux for their mentorship. We would also like to thank Joe Gesenhues and Carlos Amaro for their technical advice and assistance.
Motivation:
Millennium Development Goal 4:
Reduce Child Mortality
Accurate, controlled fluid delivery in neonatal care is vital. Infants, due to their small body mass, are extremely susceptible to improper fluid intake [Machen, 2010]. Slight fluctuations in delivery rate can be fatal.
Developed world clinics use electronic syringe pumps for IV infusion. However, high cost, power, and personnel requirements make these models inaccessible to developing world hospitals. These hospitals are then limited to using inaccurate manual methods such as gravity-fed IV bags.
Testing Results:
Conclusions:
NeoSyP is a user friendly syringe pump with the potential to save millions of lives. It solves a major need in neonatal care by providing flow rate accuracy that is inexpensive and robust to rugged developing world conditions.
Category | Specification
Accuracy | ±15%
Weight | 9 lbs. 8 oz.
Cost | $84.70 / each
Flow rates | 5-40 cc/hr flow rates
Syringe compatibility | 20, 30, 60 cc
Power Requirements | None
Target Population: Hospitals in low resource settings, serving up to 11 million premature and low birthweight neonates in Asia and Africa
Objective: Design a simple, cost-efficient, low power and easy-to-use syringe driver for the developing world
Specifications:
How NeoSyP Works:
How to Use NeoSyP:
Position Carriage
Load Syringe
Set Flow Rate
Go!
1
2
3
Measure instantaneous and average flow rates for 1 hr run
Conclusion: Flow rates are within 15% of set value
Accuracy:
Future Tests:
Robustness: Include accelerated wear testing
Ease of Use: Survey medical experts and novices on usability and intuitiveness of user interface
Robustness: Drop tests performed on acrylic housing show device can withstand drops up to 12’’.